placet experiri ...

It's great fun to make experiments

Here is a template for your own experiments and research.

What you can do with the Test program ?	1

Predefined parameters	2

1: sample-time measurement data record	2

2: Measuring data send from flash to LogView	2

Structure of the Text file for data exchange with the PC	3

Create a file for Logview	3

Hardware:	5

Analog Inputs	5

Digital inputs	5

Outputs	6

Serial Communication	6

CPU ports assignment	6

Specifications metamorphosis (maximum configuration)	8

For more information and data sheets	9

# What you can do with the Test program ?

- Test and switching of all outputs

- Testing of all analog and digital inputs

- Integration and display of two counters

- Date / Time Input (Menu 7) as an example

- Data input via the device (Menu 8) as an example

- Monitoring and data input via the PC (eg Dialer from the CD or via a terminal program, "S" for start, "E" to exit, otherwise 0-9 and "*" and "#" keys)

- Parameter transfer to the PC to a text file (use Dialer from the CD, Select “Data”, “get parameters”). Prepared for 50 integer values.

- Parameter Transfer from a text file on the PC to the Metamorphosis (use Dialer from the CD, there “Data”, “parameter Transfer”).

- Status In- and Output and Measured values cyclically sending to the PC (by PC software Dialer). Start the Dialer, Select “Display all information” or send "S" and "O" by a Terminal-Program.

- Measured values send to Logview (freeware for to show Trending). Use the Dialer then select “data”, “data to Logview”or send "S" and "U" by a Terminal-Program.

- Record data according to predefined cycle in the internal RAM and EEPROM. Read data and send it to the PC via the Dialer or a terminal-Program with "S" and "L".

- This data is written to a text file or sent directly to Logview. So data can be recorded or stored in the metamorphosis and retrieved later.

Notes:

If the data should be sent to Logview, then select in Menu 8, Parameter 2 "1". Now all the data from the memory are sent to Logview and it also displays the start time. This can then be entered manually in Logview to have the exact Time.

With the power turned off, all the recorded data is lost and the recording starts again.

Individual settings in the program are marked with *** change

# Predefined parameters

## 1: sample-time measurement data record

Here you can enter the time, how often the analog values should be logged.

- If you enter a value of 1-100, the unit is seconds.

- If you enter a value of 101-200, the unit will be minutes.

For example 102 is 2 minutes.

- If you enter a value of 201-224, the unit will be hours.

For example, 203 means 3 hours.

This means that when you for example enter 120, you have a recording interval of 20 minutes

The number of stored values in the metamorphosis is approximately 5000 16-bit values

## 2: Measuring data send from flash to LogView

The data stored in the flash can be sent to Logview. Therefore this value must be set to "1". After transmission of data, the value is again, "0".

Before that LogView must be started and select the appropriate unit and Ini-file (see below).

When uploading to the device the start time of the recording is displayed. This can be set in Logview-graphics, time format for the X-axis (below) to get the right time.

# Structure of the Text file for data exchange with the PC

Write any text for explanation, then a “:” and then the value (after the ":" the value will vbesent to the Unit!).

# Create a file for Logview

The data can be recorded in Logview. A .Ini file has to be created, where the measurements recorded are described.

In the directory there is an editor for Logview Start c:\Program Files\ LogView

V2\ open format\OpenFormatEditor.exe. With that you can create the necessary ini files for Logview very easily..

Here's an example:

First input mask for the header data

Here the measurements are described. The factor for correction can be used if needed.

In the folder “OF-information” and "How to use" there is useful information.

Store the ini file in the directory

c: \ Documents and Settings \ user name \ Application Data \ LogView \ Device \ open format stored \

You must choose now for the Device: Device selection, select the device and Port, then select Open format \ New file.

Now, the Port has to be selected.

Select at File, Settings, "Start immediately data recording "

Define the default path for the log files. There the Data are stored and can then be selected again offline.

More info on the CD on \ LogView or www.logview.info/cms/d_logview-21.phtml

# Hardware:

Analog Inputs

The input is internally connected with a 10K resistor to ground. With a little effort it could also be changed internally. But it can also be adjusted by an external shunt resistor to ground. An external resistor of 10K gives for example a total resistance of 5K (1 / R = 1/R1 + 1/R2). For accurate measurement, it is good if this resistance is about the same as range as the sensor resistance.

For the following sensors, there is a table: 10K NTC, Pt1000, PTC.

Digital inputs

Isolated inputs are used. A 5V signal is set for a short time at Terminal 47, 50, 53, 56. 24V or another voltage can also be applied but you need a series resistor. At 24 V, the series resistor is about 4.7 K. The wiring for 24V is: 24V to external Contact. Output of Contact to Input 48. 49, 51, 53

Outputs

Output 1 = Transistor Output

Output 2-7 = 10 A relay, rest is transistor

Output 15 is a 1 A relay internally wired

Relay 2 +3 and 4 +5 are each interconnected to be able to make a motor go left and right (solar Tracking f.e.). This also means relay 2 +3 have the same Input voltage and relays 4 +5 as well. In each case Contact to open and Contact to close is wired to the terminals. Max 10 A / 220 V for the Relay.

Take care!

Automatic short circuit-protection of the Load-Output with 12V and 24 V (Relay and Transistor)

For 220V short circuit-protection the must be applied externally

Serial Communication

The Baud-rate is 19200 Bd with 8 characters, no Parity, 1 Stop bit. (8, n, 1)

# CPU ports assignment

| CPU-Pin |  | Status | used for | CPU-Modul | External |
| --- | --- | --- | --- | --- | --- |
| 1 | PEN |  |  |  |  |
| 2 | PE0 | MOSI/RxD1 COM1 | MOSI/RxD1 COM1 | 112 |  |
| 3 | PE1 | MISO/TxD1 COM1 | MISO/TxD1 COM1 | 113 |  |
| 4 | PE2 | AIN0 | High Current Puls MOSFET | 104 | 43 |
| 5 | PE3 | Analog Comparator | free Input/Output | 105 | 44 |
| 6 | PE4 | PWM Output B T3/int | free PWM Output/Sensor active | 106 | 98 |
| 7 | PE5 | PWM Output C T3/int | LCD-LED-Light | 107 | 46 |
| 8 | PE6 | Counter 1 in/ Int6 | Counter 1 in / Timer 3 | 36 |  |
| 9 | PE7 | INT7/T3 Capture/int | Output_12/Load 5 | 109 |  |
| 10 | PB0 |  | NiCd charge (Relay) | 47 |  |
| 11 | PB1 | SCK, PCINT1 | SCK; PCINT 1, Interrupt Phase Loop control; Counter 2 in | 40 |  |
| 12 | PB2 |  | MUX 1 Analog in | 128 |  |
| 13 | PB3 |  | SD-Card Mosi | 127 |  |
| 14 | PB4 |  | SD-Card Miso | 38 |  |
| 15 | PB5 | PWM1:DTMF out | DTMF out | 115 |  |
| 16 | PB6 | OC1B | SD-Card CLK | 39 |  |
| 17 | PB7 | PWM Output T2 | Solar charge PWM | 117 |  |
| 18 | PG3 |  | Output_10/Load 3 | 118 |  |
| 19 | PG4 |  | Output_11/Load 4 | 119 |  |
| 20 | Reset |  | Reset | 35 |  |
| 21 | VCC |  | VCC | NC |  |
| 22 | GND |  | GND | NC |  |
| 23 | XTAL2 |  | XTAL2 | NC |  |
| 24 | XTAL1 |  | XTAL1 | NC |  |
| 25 | PD0 | SCL/int | SCL/Radio Clock | 125 | 84 |
| 26 | PD1 | SDA/int | SDA/Radio Data | 126 | 85 |
| 27 | PD2 | RxD2 | serial COM2 | 45 |  |
| 28 | PD3 | TxD2 | serial COM2 | 44 |  |
| 29 | PD4 |  | MUX 2 Analog in | 129 |  |
| 30 | PD5 |  | MUX 3 Analog in | 130 |  |
| 31 | PD6 | Counter 1 in | Freq_Noise T1 | 37 | 84 (not wired) |
| 32 | PD7 | Counter 2 in (nur M128) | free Output 14 etc | 132(CPU-Pin)/108 | 97 |
| 33 | PG0 |  | SD-Card Chip Select | 133 |  |
| 34 | PG1 |  | Output 9/Load 2 | 134 |  |
| 35 | PC0 | P9 | DE8/LCD_RS | 9 |  |
| 36 | PC1 | P10 | DE9 | 10 |  |
| 37 | PC2 | P11 | DE10 | 11 |  |
| 38 | PC3 | P12 | DE11/Input active | 12 |  |
| 39 | PC4 | P13 | Keyboard | 13 |  |
| 40 | PC5 | P14 | LCD Data | 14 |  |
| 41 | PC6 | P15 | HC573 Data | 15 |  |
| 42 | PC7 | P16 | Relay Telephone call | 16 |  |
| 43 | PG2 |  | free Output_13/Load 6/Phase Loop | 143 |  |
| 44 | PA7 | P8 | DE7 | 8 | 58 |
| 45 | PA6 | P7 | DE6 | 7 | 57 |
| 46 | PA5 | P6 | DE5 | 6 | 55 |
| 47 | PA4 | P5 | DE4 | 5 | 54 |
| 48 | PA3 | P4 | DE3/LCD_P3 | 4 | 52 |
| 49 | PA2 | P3 | DE2/LCD_P2 | 3 | 51 |
| 50 | PA1 | P2 | DE1/LCD_P1 | 2 | 49 |
| 51 | PA0 | P1 | DE0/LCD_P0 | 1 | 48 |
| 52 | VCC |  |  | 32 |  |
| 53 | GND |  |  | 31 |  |
| 54 | PF7/28 | ADC7 | Program Switch | 28 |  |
| 55 | PF6/27 | ADC6 |  | 27 | 88 |
| 56 | PF5/26 | ADC5 |  | 26 | 87 |
| 57 | PF4/25 | ADC4 |  | 25 | 85 |
| 58 | PF3/24 | ADC3 |  | 24 | 84 |
| 59 | PF2/23 | ADC2 |  | 23 | 82 |
| 60 | PF1/22 | ADC1 |  | 22 | 81 |
| 61 | PF0/21 | ADC0 |  | 21 | 80 |
| 62 | AREF |  |  |  |  |
| 63 | GND |  |  |  |  |
| 64 | AVCC |  |  |  |  |

# Specifications metamorphosis (maximum configuration)

| Power-Supply | 10-30 V |
| --- | --- |
| System-Voltage (automatic switch over) | 12 V / 24 V |
| max. Number of relay (12V, 24V, 220V) for pumps etc | 6 |
| Switching power relay outputs max. | 10A |
| Switching voltage, relay outputs | 12V / 24V / 110V / 220V AC / DC |
| Automatic short circuit-protection of the Relay Output | 12V/24V yes, 220V no (must be applied externally) |
| Latching relays (only need to save energy) | possible |
| Connection pulse valves (need a Pulse to switch) | possible |
| max. No. Transistor outputs (12V/24V) | 5 |
| Automatic short circuit-protection of the Load-Output | yes |
| free selection of the input-Typs | Voltage; Current, NTC, PTC, Pt1000, 0-20mA, 4-20mA |
| max. Number of analog inputs | 15 |
| max. Number of digital inputs | 8 Isolated |
| Max. number digital Potential-free Inputs | 8 |
| Counter-Input | 2 |
| Power-consumtion of the Unit | 15 mA |
| max.ambient temperature | -25 °C... +50 °C |
| LCD-Display | yes, 2*16 signs |
| small LCD-Display | 74 x 35 mm |
| big LCD-Display (fits only in the big Case) | 99 x 24 mm |
| Keypad | yes, 12 keys |
| Program-selector | yes, 12 positions |
| Max. number serial interfaces | 2 |
| Alarm-Beeper | Yes |
| ELV wireless sensors | Wind, Temperature, Humidity, Rain |
| max. Number of stored measurement values | 4000 16bit |
| Optional data logging on MMC / SD-card | yes, with it 16 million measured values |
| Interface to the free excellent Logging-Software Logview | yes |
| Remote control by a Windows PC (using our freeware Dialer) | yes, all functions |
| Remote control by modem, Mobilephon, GSM-Modem | yes |
| with that SMS-handling (Alarm and switches Output) | yes |
| optional connection of a cable-telephone | yes, 2 phone numbers |
| optional network / Internet-connection | yes |
| Output auxiliary-Voltage 5V, 0,5A | yes |
| optional adjustable Voltage-Output with 3V. 12V/24V, 1A | yes |
| Download of new software by the PC | yes |
| short high-current-impulses for the reducing of Sulphating | yes |
| max. cable connection (fine - / single-wire) Solar | 16 mm² |
| max. cable connection (fine - / single-wire) Relay | 2.5 mm² |
| Protection-Class | IP 32 |
| Dimension L x B x H in the standard-casing | 200 x 190 x 78 mm |
| Dimension L x B x H big Case | 290 x 260 x 115 mm |
| Operation-languages (at present) | German / English |

# For more information and data sheets

www.alternative-technology.de/Mikrocontroller System/Mikrocontroller System.html

Much fun and success with exploring and experiments! It is not always easy, Small Steps, that are my experiences. But the Internet has an answer on all questions! And at the end you always have success! Contrary to some other business.

Links

Bascom Compiler: www.mcselec.com

Support Center Bascom: http://www.mcselec.com/support-center/

Bascom forum: http://www.mcselec.com/index2.php?Parameter=com_forum&Itemid=59

For Logview latest version etc. www.logview.info

AVR Freaks: lots of good tips www.avrfreaks.net ...

www.mikrocontroller.net: Also very good

Contact

Stefan Schranner

Tel: +49 (0) 931 72 353

Mobile: +49 (0) 152 54,690,448

Internet: www.alternative-technologie.de

Email: StefanSchranner@yahoo.de